## Slide 1: Engineering Strategies

## Slide 2: Traffic Calming
Traffic calming is an approach to reducing vehicle speeds and vehicle volume on particular streets or in particular areas. Traffic calming describes a wide range of road and environmental design changes that either make it:
    more difficult for a vehicle to speed, or
    make drivers believe they should slow down for safety.
Traffic calming measures are particularly effective at reducing speeds in residential areas.
Notes: <number>
<footer>
<header>
<date/time>
In considering engineering and design changes, officers should be aware of traffic calming.

## Slide 3: What Traffic Calming is not …
Stop signs, signals, and speed limit signs, as they require enforcement.
Traffic calming is intended to be self-enforcing.
Notes: <number>
<footer>
<header>
<date/time>
Presenter/Facilitator: Ask the class, “What is meant by self-enforcing here?”

## Slide 4: Traffic Calming History
Began in Europe in 1960s as a grass roots movement to slow traffic on residential streets
Design engineers picked it up in the 1970s and were able to design “slow streets”
Applied it also to some European highways and arterial streets in 1980s

## Slide 5: Traffic Calming in U.S.
Some traffic calming as early as 1960s sprung up in several U.S. cities
Cities such as Berkeley, Seattle, and Portland had early versions of it
Many other cities now routinely use traffic calming
Traffic calming efforts now exist in each of the 50 states
Notes: <number>
<footer>
<header>
<date/time>
Sources are National Traffic Highway Safety Administration (1999), Traffic Calming: State of the Practice; traffic calming.org.
In the U.S., two cities paved the way for traffic calming, Seattle, Washington and Berkeley, California. Berkeley adopted in 1975 a citywide plan to calm traffic. Seattle was successful in securing early funding for neighborhood street improvements in 1968 in the form of a $12-million bond issue, allowing Seattle to undertake a series of traffic calming studies and demonstrations. Today, "Seattle has more experience implementing more traffic measures than any other community in the United States." One of the early demonstrations yielded some good information on what is important to accomplish when implementing traffic calming measures in a community:
Testing complex area-wide treatments before implementing them permanently,
Assessing public support for the treatment,
Conducting before-and-after studies of traffic impacts,
Including traffic accidents among the impacts studied,
Working with emergency services to address their concerns, and
Opting for the most conservative designs that will do the job.

## Slide 6: Traffic Calming Results
Speeds reduced
In some cases accidents reduced
In many cases, severity of accidents reduced
In some cases traffic volume reduced
In area-wide traffic calming schemes traffic volume not displaced, and vehicle speeds reduced
Notes: <number>
<footer>
<header>
<date/time>
Source: National Traffic Highway Safety Administration (1999), Traffic Calming: State of the Practice (pp. 116-126). Area-wide traffic schemes are those put in place in an entire neighborhood or area.

## Slide 7: Traffic Calming Now Used In:
Denmark
Sweden
The Netherlands
Germany
Japan
England
Italy
Switzerland
Canada
Australia
U.S.A.

## Slide 8: Traffic Calming 3 ways to reduce speed of vehicles
Vertical Measures – discourages speeding with vertical traffic-slowers in the road such as speed humps
Horizontal Measures – decreases speed through lateral impediments such as curves in the roadway
Narrowing – decreases speed by narrowing curb-to-curb distance so motorists slow down to adapt to changed roadway
Notes: <number>
<footer>
<header>
<date/time>
Traffic calming has two goals: reduce traffic volume and reduce traffic speeds. Reducing traffic volume involves different techniques than reducing speeds.

## Slide 9: Table of Speed Reducing Measures
Small Center Islands or Rounds
Roundabouts
Chokers
Traffic Circles
Speed Tables
Pinch-Points
Chicanes
Speed Humps
Narrowing
Horizontal
Vertical
Raised Intersections
Notes: <number>
<footer>
<header>
<date/time>
Police have been generally in favor of traffic calming as it reduces speeding problems. Fire and other Emergency Services have been against them in some communities and in favor of them in others. See Chapter VII of Traffic Calming: State of the Practice (1999) for additional information.

## Slide 10: Vertical Speed Reducing Measures
Speed Humps
Speed Tables
Speed Cushions
Notes: The next series of slides show vertical speed reducing measures

## Slide 11
Human Speed Bumps (Not recommended)
Notes: <number>
<footer>
<header>
<date/time>
It’s a joke!

## Slide 12: Speed Humps
Speed humps are rounded raised areas placed across the roadway. They are generally 3 to 4 inches high and 12 to 14 feet long (in the direction of travel), making them distinct from the shorter "speed bumps” found in many parking lots. The profile of a speed hump can be circular, parabolic, or sinusoidal. They are often tapered as they reach the curb on each end to allow unimpeded drainage.
Also know as “sleeping policemen” because they enforce speed limits 24-hours a day.
Notes: <number>
<footer>
<header>
<date/time>
Speed bumps on the other hand are usually shorter than 10 feet and cause the greatest driver discomfort at low speeds. Higher speeds over speed bumps cause damage to the vehicle. Sources for this information are National Traffic Highway Safety Administration (1999), “Traffic Calming: State of the Practice” and Michael Scott (2002),

## Slide 13: Speed Humps
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Speed Hump Profiles
Sinusoidal
Circular
Parabolic
Notes: <number>
<footer>
<header>
<date/time>
Instructor Notes: Speed humps can take different forms and traffic engineering should be familiar with the research about which type of speed hump works best under what conditions. Speed humps have been designed with different rises in different communities. Sinusoidal means shaped like or varying according to a sine curve. A Circular curve follows the lines of a circle. A Parabolic speed hump is more bowl-shaped. For further discussion on which rises produce more effective results see Chapter IV of National Traffic Highway Safety Administration (1999), Traffic Calming: State of the Practice. In years past, some jurisdictions put in speed bumps, not speed humps, and it’s important for class participants to know and recognize the difference between the two. Speed bumps, which do not work and can damage to vehicle undercarriages, may also be community members’ only experience with traffic calming. Officers should be able to share with community members that speed bumps are not recommended as speed reducers in residential neighborhoods and that speed humps are significantly different from their similarly named predecessors.

## Slide 15: Speed Hump (Portland, OR)
This speed hump is painted with chevron
markings to make it more noticeable
Notes: <number>
<footer>
<header>
<date/time>
In some communities, speed humps are called “sleeping policemen” because they enforce speed limits 24-hours a day. Sources for information and photos: National Traffic Highway Safety Administration (1999), “Traffic Calming: State of The Practice.

## Slide 16: Speed Humps
Advantages
Speed humps are relatively inexpensive;
They are relatively easy for bicycles to cross if designed appropriately;
They are very effective in slowing travel speeds
Cost is approximately $2,000 (as per Portland (OR), Sarasota (FL), and Seattle (WA)
Disadvantages
They cause a "rougher ride" for all drivers, and in some cases can cause severe pain for some people;
They force large vehicles, such as emergency vehicles to travel at slower speeds;
Some people do not find them aesthetically pleasing
Notes: <number>
<footer>
<header>
<date/time>
Source is National Traffic Highway Safety Administration (1999), Traffic Calming: State of the Practice.

## Slide 17: Speed Humps - Effectiveness
For a 12-foot hump, average of 22% decrease in the 85th percentile travel speeds, or from an average of 35.0 to 27.4 miles per hour (from a sample of 179 sites). Average of 11% decrease in accidents, or from an average of 2.7 to 2.4 accidents per year (from a sample of 49 sites).
For a 14-foot hump, average of 23% decrease in the 85th percentile travel speeds, or from an average of 33.3 to 25.6 miles per hour (from a sample of 15 sites). Average of 41% decrease in accidents, or from an average of 4.4 to 2.6 accidents per year (from a sample of 5 sites).
Similar Measures:
By lengthening the hump with a flat section in the middle, you have a Speed Table
By turning an entire crosswalk into a speed hump, you have a Raised Crosswalk, and
By raising the level of an entire intersection, you have a Raised Intersection.
Notes: <number>
<footer>
<header>
<date/time>
Source is National Traffic Highway Safety Administration (1999), Traffic Calming: State of the Practice.

## Slide 18: Speed Hump (West Palm Beach, FL)
Signage is important
to alert motorists to
reduce speeds
This 12-foot hump is combined with textured pavement to increase visibility and its speed- reducing effect
Notes: <number>
<footer>
<header>
<date/time>
Most traffic calming is concentrated in the Sunbelt and the Northwest, however, there are traffic calming measures used in cities that get snow. In these areas, such as Dayton, which averages 28 inches of snow per year, traffic calming measures are announced with signs and snowplows have rubber tipped blades to prevent damage to snow removal equipment or the traffic calming device. Communities with heavier snow levels, such as Minneapolis, Toronto, New York City and Boston also use traffic calming devices. Sources for information and photos: National Traffic Highway Safety Administration (1999), “Traffic Calming: State of The Practice.

## Slide 19: Speed Tables a.k.a. trapezoidal humps, speed platforms
Speed tables are flat-topped speed humps
Often constructed with brick or other textured materials on the flat section.
Speed tables usually let the entire wheelbase of a passenger car rest on the flat section.
Brick or other textured materials improve the appearance of speed tables, draw attention to them, enhancing safety and speed-reduction.
Notes: <number>
<footer>
<header>
<date/time>
Source: trafficcalming.org

## Slide 20: Speed Tables
Notes: <number>
<footer>
<header>
<date/time>
Source: trafficcalming.org

## Slide 21: Speed Table Naples, FL
Concrete speed table with textured pavement
to increase visibility and reduce speeds
Notes: <number>
<footer>
<header>
<date/time>
Sources for information and photos: National Traffic Highway Safety Administration (1999), “Traffic Calming: State of The Practice.

## Slide 22: Speed Tables
Advantages:
They are smoother on large vehicles (such as fire trucks) than Speed Humps, and
They are effective in reducing speeds, though not to the extent of Speed Humps
Disadvantages:
Without textured materials they are less aesthetically pleasing
Textured materials, if used, can be expensive
Cost: Approximately $2,000 –
Sarasota. FL, Portland OR, Seattle, WA
Notes: <number>
<footer>
<header>
<date/time>
Source: trafficcalming.org

## Slide 23: Speed Tables
Effectiveness:
For a 22-foot speed table, average of 18% decrease in the 85th percentile travel speeds, or from an average of 36.7 to 30.1 miles per hour; (from a sample of 58 sites).
Average of 45% decrease in accidents, or from an average of 6.7 to 3.7 accidents per year (from a sample of 8 sites).
Similar Measures:
By removing the flat section in the middle, you have a Speed Hump
By placing a crosswalk on the flat section, you have a Raised Crosswalk; and
By raising the level of an entire intersection, you have a Raised Intersection
Notes: <number>
<footer>
<header>
<date/time>
Source: trafficcalming.org

## Slide 24: Speed Cushions
A speed cushion is a variation on a standard speed hump. However, these devices do not span the entire width of the roadway but taper off at the edges. The width of the raised portion is sufficient to ensure that cars have to pass over some of the hump but may allow buses and emergency vehicles to pass over with less impact.
Cost: $5,600-$7,300
Notes: <number>
<footer>
<header>
<date/time>
These are like speed humps but do not extend all across the road. They are designed to be narrow enough to slow down cars but not to affect buses and emergency vehicles. They are usually installed in pairs, arranged across the carriageway, but single cushions are sometimes put centrally between build outs. "Three abreast" versions, and double pair arrangements have also been used. Are speed cushions noisy? A speed cushion can actually reduce the general traffic noise and the maximum vehicle noise for light vehicles, as they slow down at the cushion. It is possible that some nuisance can be caused, because of vehicles speeding up between the cushions. But this effect can be avoided if the cushions are spaced so that constant traffic speeds are encouraged along the route. Research suggests that 50m (165 ft )spacings of cushions results in very little variation in noise levels, with average speeds along the route of around 20mph.
Source: Travelwise.org.uk

## Slide 25
The speed cushion dimensions are about 7' wide, 10' long and 3" tall. Most passenger vehicle axle widths are around 6', so they cannot straddle speed cushions as emergency vehicles do.
Speed cushions are designed to slow traffic to 25 mph and lower traffic volume by 5 - 7%.
Speed Cushions

## Slide 26: Speed Cushions
Disadvantages
May divert traffic to parallel streets;
May require elimination of parking to ensure that drivers can align large vehicles over the cushions
May cause vehicles to encroach into bicycle lanes.
Advantages
Reduces vehicle speed.
Can reduce vehicular volume.
No restrictions to on-street parking
Requires minimum maintenance
Minimal impact to emergency response times
Notes: <number>
<footer>
<header>
<date/time>