## Slide 1: Horizontal Speed Reducing Measures
Chicanes
Traffic Circles
Roundabouts
Notes: The next series of slides show horizontal speed reducing measures – chicanes and traffic circles

## Slide 2: Chicanes a.k.a. deviations, serpentines, reversing curves, and twists
Chicanes are curb extensions that alternate from one side of the street to the other, forming S-shaped curves.
Chicanes can be created by alternating on-street parking, either diagonal or parallel, between one side of the street and the other. Parking bays can be created by re-striping the roadway or installing raised, landscaping islands at the ends of each parking bay.
Good for locations where speeds are a problem but noise from Speed Humps would be unacceptable
Notes: <number>
<footer>
<header>
<date/time>
Source: www.trafficcalming.org

## Slide 3: Chicanes
Notes: <number>
<footer>
<header>
<date/time>
Source: www.trafficcalming.org

## Slide 4: Chicane – Tallahassee, FL
Angled in
Angled out
This chicane uses a series of staggered jutting angles to slow traffic. By placing edged islands opposite each other (without staggering) you can create a Choker, which also slows speeds
Notes: <number>
<footer>
<header>
<date/time>
Photo source: Traffic Calming: State of The Practice. Additional source: www.trafficcalming.org.
Many cities across the U.S. have experimented with different traffic calming approaches. Particularly in earlier experimentation, not all were successes, however, this has built a better body of knowledge of what works and what does not in reducing speeds on residential streets. You may find that in your own city some traffic calming measures are insufficient or poorly designed, this however does not diminish the value of well-designed traffic calming. Many cities now design temporary traffic calming measures, and then assess whether they have the desired speed reduction effects before replacing the temporary design with a more permanent replacement, as traffic calming measures increase in popularity. Also, temporary traffic calming measures allow community members to adjust to the approach and either support or reject it in a particular location.

## Slide 5: Chicanes – Advantages and Disadvantages
Advantages
Chicanes discourage high speeds by strategic road narrowing through forced deflection; and
They are easily negotiable by large vehicles (such as fire trucks) except under heavy traffic conditions.
Disadvantages
They must be designed carefully to discourage drivers from deviating out of the appropriate lane;
Curb realignment and landscaping can be costly, particularly if there are drainage issues; and
They may require the elimination of some on-street parking.
Can cost as much as $14,000
Notes: <number>
<footer>
<header>
<date/time>
Source: www.trafficcalming.org

## Slide 6: Traffic Circles a.k.a. rotaries, intersection islands
Traffic circles are raised islands, placed in intersections, around which traffic circulates.
Good for calming intersections, especially within neighborhoods, where speeds, volumes, and safety are problems, but larger vehicles (e.g., trucks) are not as prevalent.
Notes: <number>
<footer>
<header>
<date/time>
Source: trafficcalming.org

## Slide 7: Traffic Circles
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Traffic Circle – Boulder, CO
Traffic can exit or go around the circle
This traffic circle uses low maintenance landscaping and is combined with a raised crosswalk. The circle narrows the traffic lane to slow speeding vehicles
Notes: <number>
<footer>
<header>
<date/time>
Sources for information and photos: National Traffic Highway Safety Administration (1999), “Traffic Calming: State of The Practice; www.trafficcalming.org.

## Slide 9: Traffic Circles
Advantages
Traffic Circles are effective in reducing speeds and improving safety
When designed well, they can be aesthetically pleasing
When placed at an intersection, they can calm two streets at once.
Disadvantages
They can be difficult for large vehicles (such as fire trucks) to navigate
They must be designed so that the circulating lane does not encroach on the crosswalks
They may require the elimination of some on-street parking, and
Landscaping must be maintained, either by the residents or by the municipality
Notes: <number>
<footer>
<header>
<date/time>
Source: trafficcalming.org

## Slide 10: Traffic Circles -- Effectiveness
Effectiveness
Average of 11% decrease in the 85th percentile travel speeds, or from an average of 34.1 to 30.2 mph (from a sample of 45 sites).
An average of 73% decrease in accidents, or from an average of 2.2 to 0.6 accidents per year (from a sample of 130 sites).
Similar Measures
By placing a raised island in a mid-block location, you have a Center Narrowing Island
By enlarging the intersection and the center island, inserting splitter islands at each approach, setting back the crosswalks away from the circulating lane, and implementing yield control at all approaches, you have a Roundabout
Cost varies based on materials and size of circle
Notes: <number>
<footer>
<header>
<date/time>
Source: www.trafficcalming.org

## Slide 11: Traffic Circle – Dayton, OH
Circles don’t need to circulate traffic in all cases
This small traffic circle slows vehicles speeds, even that of city busses, through this residential street. Circles slow speeds of two streets at once.
Notes: <number>
<footer>
<header>
<date/time>
Circles don’t need to circulate traffic around it in all cases. In this photo, the circle is small, allowing cars and busses to navigate along it while slowing traffic down in all four directions. Photo and information source: National Traffic Highway Safety Administration (1999), “Traffic Calming: State of The Practice.
Circles slow speeds at the intersection and perhaps for a couple hundred feet before and after the intersection. Just as with stop signs, there may be some speeding up mid-block. In Seattle, vehicle speeds at circles and leading to and from circles is monitored regularly.

## Slide 12: Monument Ave. – Richmond, VA
Notes: <number>
<footer>
<header>
<date/time>
Roundabouts are different from traffic circles. They are generally larger than traffic circles and focus on allocating right-of-way on high volume streets. While they can reduce speeds they tend to focus more on intersection control and accident reduction. The roundabouts in Boston and Washington, D.C. are old style roundabouts and have been rejected in favor of smaller rounds designed for yield at entry (yield to left).
This is Richmond’s most famous roundabout, circling the Robert E. Lee monument. Note the generous signage and lines.

## Slide 13: Stop Signs vs. Traffic Circles
Notes: This graph shows the differences in speeds approaching and departing a stop sign and driving around a traffic circle. Note the sharp acceleration by drivers departing the stop sign.

## Slide 14: Narrowing as a Speed Reducing Measure
Pinch-points, Chokers, and Small Center Islands or Rounds
Notes: Instructor Notes: The next slight shows an example of one narrowing approach – a choker. Also, another way to narrow a road to make vehicles slow down is to permit parking on both sides of a residential street.

## Slide 15: Center Island Narrowing
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Landscaping-Eugene, OR
These traffic islands in two residential areas illustrate differences between landscaped and un-landscaped mid-street measures.
Notes: <number>
<footer>
<header>
<date/time>
Landscaping adds costs but also makes some traffic calming measures more acceptable to residents. As traffic calming measures increase in popularity, many cities turn over landscaping and on-going maintenance of the island or circle to a neighborhood group to reduce city costs. There is some similarity here with the Adopt-a-Highway approaches utilized by state agencies to increase trash and weed removal along state roads.
Photos and information source: National Traffic Highway Safety Administration (1999), “Traffic Calming: State of The Practice.

## Slide 17: Choker - Australia
This Choker narrows the road from both sides of the car reducing speeds of vehicles on this residential street.
Notes: <number>
<footer>
<header>
<date/time>
Photo source: Traffic Calming: State of The Practice. Additional source: www.trafficcalming.org.
Chokers are a form of narrowing. Other forms of narrowing can be achieved with small center islands.
Some traffic calming measures in a few cities have been removed, predominantly because of poor design, which caused more, rather than fewer, problems for neighborhood residents. Currently, there are no national standards for implementing traffic calming measures, while this allows for further experimentation and innovation, it also has supported some designs that would fail to meet a national standard if set.
If students are looking for additional resources on traffic calming in the United States, the following book provides a thorough overview of traffic calming measures and lessons in the U.S. and Canada. It is downloadable from www.trafficcalming.org:
Traffic Calming: State of the Practice (1999). International Traffic Engineers and the Federal Highway Administration.
This report contains a synthesis of traffic calming experiences to date in the United States and Canada. It includes information on traffic calming in residential areas and in areas where high speed rural highways transition into rural communities. The report draws from detailed information collected on traffic calming programs in twenty featured communities, another 30 communities surveyed less extensively, and a parallel Canadian effort by the Canadian ITE (CITE) and the Transportation Association of Canada (TAC). The intended audience is transportation professionals although police and community members will find it a valuable resource.

## Slide 18: Choker
Notes: <number>
<footer>
<header>
<date/time>